## Slide 1: Object Oriented Programming
Objects, Inheritance, Encapsulation
Java
FRC Java
ArmSystem Example
Notes: Have browser with references open
Preferably with robot on
Provide background on the first two years of Java and issues

## Slide 2
PIDController
Linear Actuator
Analog Potentiometer
ArmSystem
Home Limit Switch
moveArm(speed)
moveArmUp()
moveArmDown()
moveArmTop()
moveArmBottom()
moveArmHome()
moveArmOffHome()
saveHomeSetpoint()
setArmSetpoint(ix)
moveArmSetpoint()
isOnTarget()
isTop()
isBottom()
isHome()
initArmPID()
Etc.
Notes: The entire ArmSystem combines
One (or more) linear actuators to meet the required lift capacity
An analog potentiometer (or encoder) to measure arm position
A “home” limit switch to set a standard baseline position
PID control implementation to be covered in more detail later

## Slide 3
/**
* The RobotMap is a mapping from the ports sensors and actuators are wired into
* to a variable name. This provides flexibility changing wiring, makes checking
* the wiring easier and significantly reduces the number of magic numbers
* floating around.
*/
public class RobotMap {
public static int iArmHomeLocSw = 2;
public static int iArmBotLimSw = 1;
public static int iArmTopLimSw = 0;
public static int iArmPosPot = 1;
public static int iArmMotor = 0;
public static void init() {
}
}
This version of RobotMap is used to define the port numbers for each object.
This information needs to be documented and communicated with the Electrical Team. It is the map for where things plug in to the RoboRIO.
Missing here are comments on what TYPES of ports each needs. E.g. iArmPosPot is for Analog.

## Slide 4
public class ArmLinearActuator extends Subsystem {
private final DigitalInput homeLocSw = new DigitalInput(RobotMap.iArmHomeLocSw);
private final DigitalInput scoopLimSw = new DigitalInput(RobotMap.iArmBotLimSw);
private final DigitalInput topLimSw = new DigitalInput(RobotMap.iArmTopLimSw);
private final SpeedController armLiftMotor = new Talon(RobotMap.iArmMotor);
private final Boolean invMotor = true;
Lots more stuff
This is a Subsystem Class – it defines the Arm elevation mechanism on the test robot and all the functions or processes that can be done to move the Arm.
Listed here are the definitions for the component objects, along with a Boolean that tells us “logically” what direction the motor has to spin to move the arm Up or Down, relative to the speed from a Joystick (which IMHO is backwards!)
Notes: Have eclipse open to the project.

## Slide 5
public class ArmLinearActuator extends Subsystem {
Cont.
public void ArmLinearActuator() {
if (invMotor) {
armLiftMotor.setInverted(invMotor);
}
}
public void initDefaultCommand() {
setDefaultCommand(new JoystickArmMove());
}
Housekeeping code
Method ArmLinearActuator is a “constructor” method that gets invoked when the class is instantiated. More later…
initDefaultCommand names the default command (if any) for the subsystem. In this example, it’s JoystickArmMove.
The default command will be in effect when no other command is active.

## Slide 6
public class ArmLinearActuator extends Subsystem {
Cont.
public boolean isTop() {
return !topLimSw.get();
}
public boolean isBottom() {
return !scoopLimSw.get();
}
Limit Switches for the Top and Bottom of the LinearActuator. These are DigitalInput objects, so the most common thing we need to do is “get” the Boolean value telling us if the switch is open (true) or closed (false).
There needs to be communication again between Programming and Electrical/Mechanical about the type of switch being used.
Normally Open read true unless held in.
Normally Closed read false unless held in.
Normally Open were used here, so the ! (not) inverts the Boolean to provide the logically correct true/false return.

## Slide 7
public void moveArm(double speed) {
if (isTop() == true) {
if((invMotor == true & speed < 0) || (invMotor == false & speed > 0)) {
speed = 0;
}
} else {
if (isBottom() == true) {
if((invMotor == true & speed > 0) || (invMotor == false & speed < 0)) {
speed = 0;
}
}
}
armLiftMotor.set(speed);
logArm();
}
moveArm method is given a “speed” value of type double.
It checks the top and bottom limit switchs along with the direction of travel and sets the speed to zero if motion needs to be stopped.
The validated speed is passed to the armLiftMotor.set method to drive the speed controller.
logArm sends telemetry to the dashboard.

## Slide 8
public class JoystickArmMove extends Command {
public JoystickArmMove() {
requires(Robot.armSubSys);
}
// Called just before this Command runs the first time
protected void initialize() {
}
// Called repeatedly when this Command is scheduled to run
protected void execute() {
Robot.armSubSys.moveArm(Robot.oi.joystick1.getY());
}
// Make this return true when this Command no longer needs to run execute()
protected boolean isFinished() {
return false;
}
// Called once after isFinished returns true
protected void end() {
Robot.armSubSys.stopArm();
}
// Called when another command which requires one or more of the same
// subsystems is scheduled to run
protected void interrupted() {
end();
}
}
JoystickArmMove command
Housekeeping code
requires – only one command at a time may use a subsystem.
This command passes the joystick Y axis (forward/backward) directly through to the subsystem moveArm method. NOTE that the object name is used, not the class name
The methods shown are standard for all commands, and we’ll dig more into what they’re used for in later examples.

## Slide 9: EXERCISES
Arm System
Initialize (replace current autonomous)
Fix isOnTarget logic
Capture Setpoint Values into Table
Read Setpoint Table from File
Save Setpoint Table to File
How would you handle two linear actuators?

## Slide 10
Java Basic
Tutorial
http://docs.oracle.com/javase/tutorial/
http://docs.oracle.com/javase/tutorial/java/concepts/index.html
Java Doc
http://docs.oracle.com/javase/8/docs/api/index.html
FRC Java
https://wpilib.screenstepslive.com/s/4485/m/13809
RobotBuilder
https://wpilib.screenstepslive.com/s/4485/m/26402
WPILib
http://first.wpi.edu/FRC/roborio/release/docs/java/