## Slide 1: Object Oriented Programming
Objects, Inheritance, Encapsulation
Java
FRC Java
ArmSystem Example Part 2 – Initialize Home
Notes: Have browser with references open
Preferably with robot on
Provide background on the first two years of Java and issues

## Slide 2
Linear Actuator
Analog Potentiometer
ArmSystem
Home Limit Switch
moveArm(speed)
moveArmUp()
moveArmDown()
moveArmTop()
moveArmBottom()
moveArmHome()
moveArmOffHome()
saveHomeSetpoint()
setArmSetpoint(ix)
moveArmSetpoint()
isOnTarget()
isTop()
isBottom()
isHome()
initArmPID()
Etc.
Notes: The entire ArmSystem combines
One (or more) linear actuators to meet the required lift capacity
An analog potentiometer (or encoder) to measure arm position
A “home” limit switch to set a standard baseline position
PID control implementation to be covered in more detail later

## Slide 3
/**
* The RobotMap is a mapping from the ports sensors and actuators are wired into
* to a variable name. This provides flexibility changing wiring, makes checking
* the wiring easier and significantly reduces the number of magic numbers
* floating around.
*/
public class RobotMap {
public static int iArmHomeLocSw = 2;
public static int iArmBotLimSw = 1;
public static int iArmTopLimSw = 0;
public static int iArmPosPot = 1;
public static int iArmMotor = 0;
public static void init() {
}
}
This version of RobotMap is used to define the port numbers for each object.
This information needs to be documented and communicated with the Electrical Team. It is the map for where things plug in to the RoboRIO.
Missing here are comments on what TYPES of ports each needs. E.g. iArmPosPot is for Analog.

## Slide 4
public class ArmLinearActuator extends Subsystem {
private final DigitalInput homeLocSw = new DigitalInput(RobotMap.iArmHomeLocSw);
private final DigitalInput scoopLimSw = new DigitalInput(RobotMap.iArmBotLimSw);
private final DigitalInput topLimSw = new DigitalInput(RobotMap.iArmTopLimSw);
private final SpeedController armLiftMotor = new Talon(RobotMap.iArmMotor);
private final Boolean invMotor = true;
Lots more stuff
This is a Subsystem Class – it defines the Arm elevation mechanism on the test robot and all the functions or processes that can be done to move the Arm.
Listed here are the definitions for the component objects, along with a Boolean that tells us “logically” what direction the motor has to spin to move the arm Up or Down, relative to the speed from a Joystick (which IMHO is backwards!)
Notes: Have eclipse open to the project.

## Slide 5
public class ArmLinearActuator extends Subsystem {
Cont.
public boolean isTop() {
return !topLimSw.get();
}
public boolean isBottom() {
return !scoopLimSw.get();
}
public boolean isHome() {
return !homeLocSw.get();
}
Limit Switches for the Top and Bottom of the LinearActuator.
Plus a “Home” switch to tell us when the arm is in a known position. This provides a point of reference for future angle settings.
There needs to be communication again between Programming and Electrical/Mechanical about the type of switch being used.
Normally Open read true unless held in.
Normally Closed read false unless held in.
Normally Open were used here, so the ! (not) inverts the Boolean to provide the logically correct true/false return.

## Slide 6
public void moveUp() {
double speed = 1 * invSpeed;
moveArm(speed);
}
public void moveDown() {
double speed = -1 * invSpeed;
moveArm(speed);
}
public void stopArm() {
if (armPID.isEnabled()) {
armPID.reset();
armPID.disable();
}
moveArm(0);
}
Fixed operation move methods to adjust the arm up or down or stopped as specified.
They use the common “moveArm” method.
Why not have the calling process directly invoke the moveArm with an appropriate speed setting?
Which would be better?

## Slide 7
public class ArmOffHome extends Command {
public ArmOffHome() {
requires(Robot.armSubSys);
}
// Called just before this Command runs the first time
protected void initialize() {
}
// Called repeatedly when this Command is scheduled to run
protected void execute() {
Robot.armSubSys.moveUp();
}
// Make this return true when this Command no longer needs to run execute()
protected boolean isFinished() {
return !Robot.armSubSys.isHome();
}
// Called once after isFinished returns true
protected void end() {
Robot.armSubSys.stopArm();
}
// Called when another command which requires one or more of the same
// subsystems is scheduled to run
protected void interrupted() {
end();
}
}
ArmOffHome command
Housekeeping code
requires – only one command at a time may use a subsystem.
This command invokes the moveUp method until it is NOT on the home position limit switch.
At end, it stops the arm motor. Another specifically named command. It could also invoke the moveArm with a speed of zero.
What are the advantages to either way?
Note that if interrupted, it will still stop the motor.

## Slide 8
public class ArmSetHome extends Command {
public ArmSetHome() {
requires(Robot.armSubSys);
}
protected void initialize() {
}
// Called repeatedly when this Command is scheduled to run
protected void execute() {
Robot.armSubSys.moveDown();
}
// Make this return true when this Command no longer needs to run execute()
protected boolean isFinished() {
if (Robot.armSubSys.isHome()) {
Robot.armSubSys.newHomePID();
}
return Robot.armSubSys.isHome() || Robot.armSubSys.isBottom();
}
protected void end() {
Robot.armSubSys.stopArm();
}
protected void interrupted() {
end();
}
}
ArmSetHome command
This command invokes the move Down method until it is either on the Home or the Bottom switch. (Checking the bottom is a safety escape just in case it was already below the home switch when moveDown was invoked – otherwise the command would continue until interrupted.)
When the Home switch is detected it invokes a method that we’ll look at in part 3 of this system.

## Slide 9
public class HomeArm extends CommandGroup {
public HomeArm() {
requires(Robot.armSubSys);
addSequential(new ArmOffHome());
addSequential(new ArmSetHome());
}
}
public class Robot extends IterativeRobot {
public void robotInit() {
RobotMap.init();
armSubSys = new ArmLinearActuator();
oi = new OI();
autonomousCommand = new HomeArm();
}
HomeArm command group (list of commands done in sequence or parallel)
This command group is defined for use in autonomous phase of the competion.
Robot is the base class for all FRC robots and includes the methods invoked by the various states of the robot as supported by the Driver’s Station and Competition Field System.
But – this is not a good place for this particular function. Homing mechanisms should be done at power-up, not when we’re trying to score points!

## Slide 10: EXERCISE
Arm System
Move the current Autonomous Command to an Initialize process.
Autonomous is done during competition.
Wastes time needed to score.
Initialize is done at power-up so everything is prepped before the game begins.

## Slide 11
Java Basic
Tutorial
http://docs.oracle.com/javase/tutorial/
http://docs.oracle.com/javase/tutorial/java/concepts/index.html
Java Doc
http://docs.oracle.com/javase/8/docs/api/index.html
FRC Java
https://wpilib.screenstepslive.com/s/4485/m/13809
RobotBuilder
https://wpilib.screenstepslive.com/s/4485/m/26402
WPILib
http://first.wpi.edu/FRC/roborio/release/docs/java/