## Slide 1: FRC 4662 Programming
Who What When Why – and HOW

## Slide 2: Roborio
National Instruments
ARM processor
Linux
Custom for FIRST

## Slide 3
Languages
Labview – National Instruments (proprietary)
4662 used this the first two years
Drag-n-drop icons for objects
“Wire” together to control data and decision flow
Provided Driver Station and some RoboRIO utility code are in Labview
Java – Sun 1995 (now Oracle)
4662 on its third year now C++ - http://www.cplusplus.com/info/history/
used on Arduino – runs the LED string on the Competition Robot
Python – unofficial and volunteer supported
https://robotpy.github.io/projects/
FIRST Sponsor WPI (Worchester Polytechnic Institute)
Robotics program participates in DARPA challenge events
Has interns (grad students) write FIRST libraries for Java and C++
Java documentation http://first.wpi.edu/FRC/roborio/release/docs/java/
Hosts a lot of FIRST training material like this https://wpilib.screenstepslive.com/s/4485

## Slide 4
Summer Learning - Test Robot Electronics
Actuators
Motors and gearboxes for drive system
Linear Actuator (motorized screw jack)
Speed Controllers
Talon SRX (CTRE)
Talon (now obsolete, available as a discontinued item)
Sensors
Quadrature Encoder
reads rotation speed, distance, and direction
http://www.digikey.com/product-detail/en/AMT102-V/102-1307-ND/827015
Potentiometer
reads position on a rotary scale
can be adapted to a linear scale with a “string” potentiometer
amazon.com search on linear potentiometer 10k
Limit Switches
AndyMark

## Slide 5: ARM LIFT
AndyMark Snowblower Motor
All-thread (3/8”)
Misc plumbing parts
Potentiometer
Limit Switches
Also pictured – Gyroscope for Drive System

## Slide 6: Actuator - ARmSystem
Command Based
Adopts some “Best Practices” seen in other team’s code samples (NUTRONS)
Java Class Encapsulation Example
PID Controller using Potentiometer
Needs work
  Initialize routine to save “home” position
  Fix the On Target method
  Allow updates to Target Table
  Read/Write table from RoboRIO stored file

## Slide 7: Drive system
RoboRIO
Talon SRX with Encoder and Limit Switch Breakout
2 CIM Drive
Gearbox

## Slide 8: Drive - PIDLing2gyro
Command Based
Pre “Best Practices” (as delivered from FRC provided RobotBuilder)
PID Encoder control using Talon SRX connected on Right side drive
Gyro read – not incorporated into drive
Needs Work
  PID Encoder control of both Left and Right drive for distance
  PID Gyro control of Left and Right drive for heading (self-steering)
  HINT – Nutron code base does this and a lot more (link from Chief Delphi to Github)
  isStuck/inTrouble methods

## Slide 9
Shopping
AndyMark http://www.andymark.com/Default.asp
FRC major supplier
Cross The Road Electronics http://www.ctr-electronics.com/
FRC custom electronics
VEX Robotics http://www.vexrobotics.com/vexpro
FRC drive parts and electronics
Digi-key http://www.digikey.com/en
electronics and connectors (voucher)
Mouser http://www.mouser.com/
electronics and connectors
Amazon http://amazon.com
learn to search (potentiometers, bearings, rod ends, etc.)
eBay http://ebay.com
learn to search (linear actuators, Anderson powerpole, etc.)
Hansen Hobbies http://www.hansenhobbies.com/
bulk PWM cable parts
Surplus Gizmos http://www.surplusgizmos.com/
surplus electronics and tech parts shop in Hillboro (on Cornelius Pass Road)

## Slide 10
References
FIRST http://www.firstinspires.org/robotics/frc
Oregon FIRST http://oregonfirst.org/
National Instrumets https://decibel.ni.com/content/community/academic/student_competitions/frc
Chief Delphi (FRC Discussion Forum) https://www.chiefdelphi.com/forums/index.php
FRC 2016 Control System https://wpilib.screenstepslive.com/s/4485
Java Training http://docs.oracle.com/javase/tutorial/
Java Docs http://docs.oracle.com/javase/8/docs/api/
Java WPILib http://first.wpi.edu/FRC/roborio/release/docs/java/
Eclipse https://eclipse.org/
Github https://github.com/